SECTION 1 – PRODUCT AND COMPANY IDENTIFICATION

Product Name 	Wood Kraft – High Grade Furniture Polish

Updated Date	August 12, 2016

Company	Encore Industrial Products	Transportation Emergency (24 Hour) Contact

P.O. Box 300	 North America:	     1-877-703-3044 Ex. 405

Barker, TX 77413-0300

Phone Number 	(281) 944-4777

(877) 703-3044

Fax (281) 944-4778	      Medical Emergencies:

Contact your local Poison Control Center.

Transportation

DOT: CONSUMER COMMODITY, ORM-D

IATA: CONSUMER COMMODITY, ORM-D

IMDG: CONSUMER COMMODITY, ORM-D

SECTION 2 – HAZARDS IDENTIFICATION

Classification:

Aspiration Hazard - Category 1

Aerosol - Category 3

Pictograms:

Signal Word:

Warning

Hazardous Statements - Physical:

H229 - Pressurized container: May burst if heated

Hazardous Statements - Health:

H304 - May be fatal if swallowed and enters airways

Precautionary Statements - General:

P101 - If medical advice is needed, have product container or label at hand.

P102 - Keep out of reach of children.

P103 - Read label before use.

Precautionary Statements - Prevention:

P210 - Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. No smoking.

P251 - Do not pierce or burn, even after use.

Precautionary Statements - Response:

P301 + P310 - IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician.

P331 - Do NOT induce vomiting.

Precautionary Statements - Storage:

P405 - Store locked up.

P410 - Protect from sunlight.

P412 - Do not expose to temperatures exceeding 50 °C/122 °F.

Emergency Overview

Hazard Classification: Aerosol Class 2	Signal Word(s): Warning/Irritant

SECTION 3 – COMPOSITION / INFORMATION ON INGREDIENTS

CAS 				Chemical Name 				% by Weight

0007732-18-5 			WATER 					48% - 86%

0064741-66-8			LIGHT ALKYLATE NAPHTHA 		6% - 12%

0000075-37-6 			DIFLUOROETHANE 			4% - 9%

0000074-98-6 		PROPANE 			4% - 9%

SECTION 4 – FIRST AID MEASURES

Inhalation:

Remove source of exposure or move person to fresh air and keep comfortable for breathing.

If exposed/feel unwell/concerned: Call a POISON CENTER/doctor.

Eliminate all ignition sources if safe to do so.

Eye Contact:

Remove source of exposure or move person to fresh air. Rinse eyes cautiously with lukewarm, gently flowing water for several minutes,

while holding the eyelids open. Remove contact lenses, if present and easy to do. Continue rinsing for a duration of 15-20 minutes. Take

care not to rinse contaminated water into the unaffected eye or onto the face. If eye irritation persists: Get medical advice/attention.

Skin Contact:

Take off immediately all contaminated clothing, shoes and leather goods (e.g. watchbands, belts). Gently blot or brush away excess

product. Wash with plenty of lukewarm, gently flowing water for a duration of 15-20 minutes. Call a POISON CENTER/doctor if you feel

unwell. Store contaminated clothing under water and wash before reuse or discard.

Ingestion:

Rinse mouth. Do NOT induce vomiting. Immediately call a POISON CENTER/doctor. If vomiting occurs naturally, lie on your side, in the

recovery position.

Never give anything by mouth to an unconscious or convulsing victim. Keep person warm and quiet.

SECTION 5 – FIRE FIGHTING MEASURES

Suitable Extinguishing Media:

Use water, fog, dry chemical, or carbon dioxide.

Carbon dioxide can displace oxygen. Use caution when applying carbon dioxide in confined spaces. Simultaneous use of foam and water

on the same surface is to be avoided as water destroys the foam.

Unsuitable Extinguishing Media:

Water may be ineffective but can be used to cool containers exposed to heat or flame.

Specific Hazards in Case of Fire:

Contents under pressure. Keep away from ignition sources and open flames. Exposure of containers to extreme heat and flames can

cause them to rupture often with violent force.

Aerosol cans may rupture when heated.

Heated cans may burst.

In fire, will decompose to carbon dioxide, carbon monoxide

Fire-Fighting Procedures:

Isolate immediate hazard area and keep unauthorized personnel out. Stop spill/release if it can be done safely. Move undamaged

containers from immediate hazard area if it can be done safely. Water spray may be useful in minimizing or dispersing vapors and to

protect personnel.

Dispose of fire debris and contaminated extinguishing water in accordance with official regulations.

Special Protective Actions:

Wear protective pressure self-contained breathing apparatus (SCBA)and full turnout gear.

Care should always be exercised in dust/mist areas.

SECTION 6 – ACCIDENTAL RELEASE MEASURES

Emergency Procedure:

Flammable/combustible material.

ELIMINATE all ignition sources (no smoking, flares, sparks, or flames in immediate area). Stay upwind; keep out of low areas.

Immediately turn off or isolate any source of ignition. Keep unnecessary people away; isolate hazard area and deny entry. Do not touch or

walk through spilled material. Clean up immediately. Use absorbent sweeping compound to soak up material and put into suitable

container for proper disposal.

Recommended Equipment:

Positive pressure, full-face piece self-contained breathing apparatus(SCBA), or positive pressure supplied air respirator with escape SCBA

(NIOSH approved).

Personal Precautions:

ELIMINATE all ignition sources (no smoking, flares, sparks, or flames in immediate area). Use explosion proof equipment. Avoid breathing

vapor. Avoid contact with skin, eye or clothing. Do not touch damaged containers or spilled materials unless wearing appropriate protective

clothing.

Environmental Precautions:

Stop spill/release if it can be done safely. Prevent spilled material from entering sewers, storm drains, other unauthorized drainage systems

and natural waterways by using sand, earth, or other appropriate barriers.

SECTION 7 – HANDLING AND STORAGE

General:

For industrial and institutional use only.

For use by trained personnel only.

Keep away from children.

Wash hands after use.

Do not get in eyes, on skin or on clothing.

Do not breathe vapors or mists.

Use good personal hygiene practices.

Eating, drinking and smoking in work areas is prohibited.

Remove contaminated clothing and protective equipment before entering eating areas.

Eyewash stations and showers should be available in areas where this material is used and stored.

Ventilation Requirements:

Use only with adequate ventilation to control air contaminants to their exposure limits. The use of local ventilation is recommended to

control emissions near the source.

Storage Room Requirements:

Keep container(s) tightly closed and properly labeled. Store in cool, dry, well-ventilated areas away from heat, direct sunlight and

incompatibilities. Store in approved containers and protect against physical damage. Keep containers securely sealed when not in use.

Indoor storage should meet OSHA standards and appropriate fire codes. Containers that have been opened must be carefully resealed to

prevent leakage. Empty container retain residue and may be dangerous.

Do not cut, drill, grind, weld, or perform similar operations on or near containers. Do not pressurize containers to empty them. Ground all

structures, transfer containers and equipment to conform to the national electrical code. Use procedures that prevent static electrical

sparks. Static electricity may accumulate and create a fire hazard.

Store at temperatures below 120°F.

SECTION 8 – EXPOSURE CONTROLS / PERSONAL PROTECTION

Eye Protection:

Chemical goggles, safety glasses with side shields or vented/splash proof goggles. Contact lenses may absorb irritants. Particles may

adhere to lenses and cause corneal damage.

Skin Protection:

Wear gloves, long sleeved shirt, long pants and other protective clothing as required to minimize skin contact.

Use of gloves approved to relevant standards made from the following materials may provide suitable chemical protection: PVC, neoprene

or nitrile rubber gloves. Suitability and durability of a glove is dependent on usage, e.g. frequency and duration of contact, chemical

resistance of glove material, glove thickness, dexterity. Always seek advice from glove suppliers. Contaminated gloves should be replaced.

Chemical-resistant clothing is recommended to avoid prolonged contact. Avoid unnecessary skin contact.

Respiratory Protection:

If engineering controls do not maintain airborne concentrations to a level which is adequate to protect worker, a respiratory protection

program that meets or is equivalent to OSHA 29 CFR 1910.134 and ANSI Z88.2 should be followed. Check with respiratory protective

equipment suppliers. Where air-filtering respirators are suitable, select an appropriate combination of mask and filter. Select a filter suitable

for combined particulate/organic gases and vapors.

When spraying more than one half can continuously or more than one can consecutively, use NIOSH approved respirator.

SECTION 9 – PHYSICAL AND CHEMICAL PROPERTIES

Physical and Chemical Properties

Density 			8.00000 lb/gal

Density VOC 		1.34400 lb/gal

% VOC 			16.80000%

VOC Actual 		1.34400 lb/gal

VOC Actual 		161.05152 g/l

Appearance 		N.A.

Odor Threshold 		N.A.

Odor Description 		N.A.

pH			 8.9

Water Solubility 		Emulsion

Flammability 		Will not burn

Flash Point Symbol 	N.A.

Flash Point 		N.A.

Viscosity 		N.A.

Lower Explosion Level 	N.A.

Upper Explosion Level 	N.A.

Melting Point 		N.A.

Vapor Density 		Slower than ether

Freezing Point 		N.A.

Low Boiling Point 		212 °F

High Boiling Point 		N.A.

Decomposition Pt 		0

Auto Ignition Temp	 	N.A.

Evaporation Rate 		Slower than ether

SECTION 10 – STABILITY AND REACTIVITY

Stability:

Stable.

Conditions to Avoid:

High temperatures

Incompatible Materials:

None known.

Hazardous Reactions/Polymerization:

Will not occur.

Hazardous Decomposition Products:

In fire, will decompose to carbon dioxide, carbon monoxide.

SECTION 11 – TOXICOLOGICAL INFORMATION

Skin Corrosion/Irritation:

Overexposure will cause defatting of skin.

Serious Eye Damage/Irritation:

Overexposure will cause redness and burning sensation.

Carcinogenicity:

No data available

Germ Cell Mutagenicity:

No data available

Reproductive Toxicity:

No data available

Respiratory/Skin Sensitization:

No data available

Specific Target Organ Toxicity - Single Exposure:

No data available

Specific Target Organ Toxicity - Repeated Exposure:

No data available

Aspiration Hazard:

May be fatal if swallowed and enters airways

Acute Toxicity:

Inhalation: effect of overexposure include irritation of respiratory tract, headache, dizziness, nausea, and loss of coordination. Extreme

overexposure may result in unconsciousness and possibly death.

SECTION 12 – ECOLOGICAL INFORMATION

Toxicity:

No data available.

Persistence and Degradability:

No data available.

Bio-Accumulative Potential:

No data available.

Mobility in Soil:

No data available.

Other Adverse Effects:

No data available.

SECTION 13 – DISPOSAL CONSIDERATIONS

Disposal Methods

Under RCRA, it is the responsibility of the user of the product, to determine a the time of disposal whether the product meets RCRA criteria

for hazardous waste. Waste management should be in full compliance with federal, state, and local laws.

Empty containers retain product residue which may exhibit hazards of material, therefore do not pressurize, cut, glaze, weld or use for any

other purposes. Return drums to reclamation centers for proper cleaning and reuse.

SECTION 14 – TRANSPORT INFORMATION

Identification	Proper		Hazardous	Packaging

Shipment	Number	Shipping Name		Classification      	Group

US DOT	None	CONSUMER COMMODITY		ORM-D	None

IATA (air)	None	CONSUMER COMMODITY			ORM-D	None

IMDG (vessel)	None		CONSUMER COMMODITY		ORM-D	None

SECTION 15 – REGULATORY INFORMATION

SECTION 16 – OTHER INFORMATION

Legend

ACGIH	American Conference of Governmental 	ICL	In-Commerce List (Canada)

Industrial Hygienists	IMO	International Maritime Organization

CAA	Clean Air Act	N/A	Not Applicable

CAS	Chemical Abstract Service	NDSL	Non-Domestic Substances List (Canada)

CERCLA	CERCLA Hazardous Substances	N/E	Not Established

CFR	Code of Federal Regulations	NTP	National Toxicology Program

DOT	Department of Transportation	OSHA	Occupational Safety & Health Administration

DSL	Domestic Substances List (Canada)	PEL	Permissible Exposure Limits

EINECS	European Inventory of Existing 	RCRA	Resource Conservation and Recovery Act

Chemical Substances	SARA	Superfund Amendments and Reauthorizations Act

EPA	Environmental Protection Agency	TLV	Threshold Limit Values

FDA	Food and Drug Administration	TQ	Threshold Quantities

HPA	Hazardous Products Act (Canada)	TWA	Time Weighted Average

IARC	International Agency for Research on Cancer	VOC	Volatile Organic Compounds

IATA	International Air Transport Association	WHMIS	Workplace Hazardous Materials Information System

This document is intended to provide a brief summary of our knowledge and guidance regarding the use of this material. The information set forth herein has been compiled from sources considered to be dependable and is believed to be accurate as of the date of publication. This information is offered in good faith by Encore Industrial and no warranty, expressed or implied is made. The user assumes all liability for any damage or injury resulting from misuse, from any failure to adhere to recommended practices or from any hazards inherent in the nature of the product.