SECTION 1 – PRODUCT AND COMPANY IDENTIFICATION

Product Name 	Drain Stream - Industrial Drain Flow Treatment

Updated Date	October 26, 2020

Supersedes Date	February 16, 2016

Company	Encore Industrial Products	Transportation Emergency (24 Hour) Contact

P.O. Box 300	  CHEM TELL :		 800 -255- 3924

Barker, TX 77413-0300	  North America:	     1-877-703-3044 Ex. 405

Phone Number 	(281) 944-4777

(877) 703-3044

Fax (281) 944-4778	      Medical Emergencies:

Contact your local Poison Control Center.

Transportation

DOT: UN 1823, Sodium Hydroxide, Solid, 8, II - (See Section 14)

IATA: UN 1823, Sodium Hydroxide, Solid, 8, II - (See Section 14)

IMDG: UN 1823, Sodium Hydroxide, Solid, 8, II - (See Section 14)

SECTION 2 – HAZARDS IDENTIFICATION

Emergency Overview

Hazard Classification:					Signal Word(s): Danger

- Pyr. Sol. 1 – Catches fire spontaneously if exposed to air

- Water-react. 2 – In contact with water releases flammable gas

- Skin Corr. 1A – Causes sever skin burns and eye damage.

- Eye Dam. 1 – Causes serious eye damage.

Hazard Symbol(s):

Hazard Statement:		 In contact with water releases flammable gases.

Causes severe skin burns and eye damage.

Precautionary Statements:

- Keep away from heat, hot surfaces, open flames. -No Smoking

- Do not allow contact with water

- Do not breathe vapors, spray, mist, fume

- Wash hands, forearms, and face thoroughly after handling

- Wear eye protection, face protection, protective gloves.

- IF SWALLOWED: Rinse mouth. DO NOT indue vomiting.   					(Continued on next page)

- IF ON SKIN (OR HAIR): Take off immediately all contaminated clothing. Rinse skin with water/shower.

- IF INHALED: Remove person to fresh air and keep comfortable for breathing.

- IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses if present and easy to do. Continue Rinse. Immediately call a doctor.

- Specific Treatment (see First Aid measures on this label)

- Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages.

- Wash contaminated clothing before reuse.

- IN CASE OF FIRE: Use ABC powder to extinguish.

- Store in a dry place. Store in a closed container.

- Store locked up.

- Dispose of contents/container to an approved waster disposal plant.

Other hazards not contributing to the classification: Reacts VIOLENTLY with water.

SECTION 3 – COMPOSITION / INFORMATION ON INGREDIENTS

Ingredients considered hazardous as defined by OSHA, 29 CFR 1910.1200, WHMIS under the HPA (Canada),

or ESIS (Europe).

Chemical Name	CAS Number		Other Limits	Wt %	                    	GHS CLASSIFICATION

Caustic Soda		1310-73-2			58.8-78.4%		                Met. Corr. 1, H290    Skin Corr. 1A, H314

Sodium Nitrate		7631-994			5-20%		               Ox. Sol. 3, H272      Acute Tox. 4 (Oral), H302

Full text of H-statements: see section 16

Remaining ingredients are non-hazardous and/or present at amounts below reportable limits and considered confidential.

SECTION 4 – FIRST AID MEASURES

General                         Never give anything by mouth to an unconscious person. If you feel unwell, seek medical advice. (show the label where 	possible.

Eye Contact	Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue Rinsing. 			Immediately call a POISON CENTER or doctor/physician.

Skin Contact	Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. Immediately call a POISON CENTER or a doctor/physician.

Ingestion	Rinse mouth. Do NOT induce vomiting. Immediately call a POISON CENTER or doctor/physician.

Inhalation	Remove victim to fresh air and keep at rest in a position comfortable for breathing. Immediately call a POLISON CENTER or doctor/physician.

Symptoms/injuries – Causes sever skin burns and eye damage.

Symptoms injuries after eye contact- Causes serious eye damage.

Indication of any immediate medical attention or special treatment needed

- Treat symptomatically

SECTION 5 – FIRE FIGHTING MEASURES

Extinguishing Media			Foam. Dry powder. Carbon Dioxide. Sand. DO NOT use heavy water stream,.

Special Hazards arising from the substance or mixture

Explosive Hazard			Heat may build, rupturing closed containers, spreading fire and increasing risk of burns and 					injuries.

Reactivity			Corrosive Vapors.

Fire Fighting Instructions			Use water spray or fog for cooling exposed containers. Exercise caution when fighting any chemical fire. Prevent fire-fighting water from entering environment. Fight fire remotely due to the risk of explosion.

Protection during firefighting			Do not enter fire area without proper protective equipment, including respiratory protection.

SECTION 6 – ACCIDENTAL RELEASE MEASURES

General Measure		No open flames. No smoking.

Emergency Procedures 	Evacuate unnecessary personnel.

For Emergency Responders	Equip cleanup crew with proper protection. Ventilate area.

Containment/Cleanup	Avoid release into the environment. On land, sweep or shovel into suitable containers. Minimize generation of dust. Store away from other materials.

Reference Section 8 for exposure controls and personal protection.

SECTION 7 – HANDLING AND STORAGE

Precautions for Safe Handling

Additional Hazards when processed 	Hazardous waste due to potential risk of explosion.

Precautions for safe handling		Wash hands and other exposed areas with mild soap and water before eating, 					drinking, or smoking and when leaving work. Provide good ventilation in 					process area to prevent formation of vapor. Take a precaution to avoid 					mixing with combustible materials. Do NOT breather vapors, mist, spray, 					fume, dust. Avoid contact during pregnancy/while nursing.

Hygiene measures		Wash hands thoroughly after handling.

Storage	 Store in a cool dry area. Keep container tightly sealed and protected from moisture and water. Product is corrosive. Do not get on skin, eyes, or clothing. If spilled on clothing, remove clothing and flush off exposed skin with water. Do not take internally. Can be fatal if swallowed Avoid breathing dust;

SECTION 8 – EXPOSURE CONTROLS / PERSONAL PROTECTION

Control Parameters  	Industrial Setting: Refer to Section 3 for ingredients with occupational exposure limits.

Engineering Controls	 For industrial settings, use in well ventilated area.

Personal Protective	Respiratory protection: Local exhaust. As required to protect from acidic vapors and mist.

Equipment		Eye/Face: Safety glasses or goggles.

Skin: Chemical resistant gloves. Splash apron.

Work Hygienic Practices	Always follow good hygienic work practices.

SECTION 9 – PHYSICAL AND CHEMICAL PROPERTIES

Color and Appearance	white granules with silver flakes	VOC Content	N/D

Odor			No odor	Boiling Point	NA

pH				greater than 13	Melting Point	NA

Specific Gravity		1.0	Vapor Density	NA

Flash Point		None	Solubility in Water	90%

SECTION 10 – STABILITY AND REACTIVITY

Chemical Stability:		Stable.

Conditions to Avoid:		Do not store in metal containers or in high humidity and extreme heat.

Incompatible Materials:	Do not mix with other chemicals; Extreme heat can be generated upon direct contact with acids, many metals, solvents, etc;

Hazardous Decomposition 	None

Products

Hazardous Polymerization	Will not occur.

SECTION 11 – TOXICOLOGICAL INFORMATION

Toxicity Tests		Data is not available.

Potential Health Effects 	Acute Eye: Irritation, redness, or burning sensation.

Acute Skin: Irritation, redness, or burning.

Acute Inhalation: Irritation, burns and tissue destruction in respiratory tract.

Acute Ingestion: Small amounts may cause nausea, cramps. Large amounts may be harmful.

Chronic Effects: Possible visual impairment to include blindness.

Carcinogenicity: Not expected to be carcinogenic.

SECTION 12 – ECOLOGICAL INFORMATION

Ecological Tests: Data is not available.

Environmental Impact: The product ingredients are expected to be safe for the environment at concentrations predicted under normal use and accidental spill scenarios. Packaging components are compatible with the conventional solid waste management practices.

SECTION 13 – DISPOSAL CONSIDERATIONS

Disposal Methods	Dispose in accordance with all applicable federal, state, and local regulations.

SECTION 14 – TRANSPORT INFORMATION

Identification	Proper		Hazardous	Packaging

Shipment	Number	Shipping Name		Classification      	Group

US DOT	1823	Compound		Corrosive	3

IATA (air)	1823	Compound			Corrosive	3

IMDG (vessel)	1823		Compound		Corrosive	3

SECTION 15 – REGULATORY INFORMATION

USA	FDA	This product is regulated as an Over-The-Counter (OTC) drug under the Federal Food, Drug,

and Cosmetics Act and complies with FDA regulations.

EPA	SARA Title III Sections 302/304, 311/312, and 313 chemical listings: None or none present

In regulated quantities.

CAA Section 112 listings (TQ): None

CERLCA Reportable Quantity (RQ): None

California Proposition 65: This product is not subject to warning labeling.

State Right-To-Know	The following ingredients are present in the finished product and

are listed on the following state right-to-know lists:

Ingredient	CAS No.	Percent	State

Sodium Hydroxide 	1310-73-2	50-70%	N/A

Canada	This product is regulated as a Natural Health Product (NHP) under the Food and Drugs Act and complies

with Health Canada regulations. All chemical components of this product are listed on DSL, NDSL, ICL

or exempt.

Europe	EU Classification: Non-hazardous

EU Risk Phrases: None

EU Safety Phrases: S2 – Keep out of reach of children. S46 – Avoid contact with eyes.

SECTION 16 – OTHER INFORMATION

Legend

ACGIH	American Conference of Governmental 	ICL	In-Commerce List (Canada)

Industrial Hygienists	IMO	International Maritime Organization

CAA	Clean Air Act	N/A	Not Applicable

CAS	Chemical Abstract Service	NDSL	Non-Domestic Substances List (Canada)

CERCLA	CERCLA Hazardous Substances	N/E	Not Established

CFR	Code of Federal Regulations	NTP	National Toxicology Program

DOT	Department of Transportation	OSHA	Occupational Safety & Health Administration

DSL	Domestic Substances List (Canada)	PEL	Permissible Exposure Limits

EINECS	European Inventory of Existing 	RCRA	Resource Conservation and Recovery Act

Chemical Substances	SARA	Superfund Amendments and Reauthorizations Act

EPA	Environmental Protection Agency	TLV	Threshold Limit Values

FDA	Food and Drug Administration	TQ	Threshold Quantities

HPA	Hazardous Products Act (Canada)	TWA	Time Weighted Average

IARC	International Agency for Research on Cancer	VOC	Volatile Organic Compounds

IATA	International Air Transport Association	WHMIS	Workplace Hazardous Materials Information System

This document is intended to provide a brief summary of our knowledge and guidance regarding the use of this material. The information set forth herein has been compiled from sources considered to be dependable and is believed to be accurate as of the date of publication. This information is offered in good faith by Encore Industrial and no warranty, expressed or implied is made. The user assumes all liability for any damage or injury resulting from misuse, from any failure to adhere to recommended practices or from any hazards inherent in the nature of the product.